## Slide 2
Study of Water Scarcity Due to Climate Change
Rainwater Harvesting as a Solution for Regi Model Town Zones 3 & 4
Prepared from the provided data and sample presentation

## Slide 3
02
Project Team & Study Scope
Rainwater harvesting design for residential plots in Regi Model Town Zones 3 and 4.
Name | Reg. No. | Class No.
Hamid Ullah Khan | 22PWCIV5948 | 163(P)
Syed Sumair Ali | 22PWCIV5900 | 190(P)
Zabi Ullah Khan | 22PWCIV5814 | 31(U)
Muhammad Fazeel | 22PWCIV5896 | 181(P)
• Data-driven rainfall and IDF analysis
• Rooftop catchment calculations from Regi by-laws
• Practical pipe, filter and tank sizing
System concept for domestic non-potable water use

## Slide 4
03
Why Rainwater Harvesting Matters
Urban water stress can be reduced by capturing seasonal rooftop runoff before it is lost as drainage flow.
Non-potable reuse
Design focus
Zone 3 & 4
Study site
• Reduces municipal demand for gardening and washing
• Provides local resilience during dry months
• Uses roof area already available within residential plots
Project intent: design a simple, maintainable and scalable RWH model for 5 Marla, 10 Marla and 1 Kanal plots.

## Slide 5
04
Study Area: Regi Model Town
Residential plots are assessed using the by-law roof and open-space proportions for Zones 3 and 4.
Plot category | Total plot area | Rooftop area | Free space
5 Marla | 1,361.25 ft² | 1,020.94 ft² | 25%
10 Marla | 2,722.50 ft² | 1,769.63 ft² | 35%
1 Kanal | 5,445.00 ft² | 3,375.90 ft² | 38%
• Rooftop area drives harvest volume
• Free space drives demand for irrigation
• By-laws support plot-wise sizing
By-law table used as the design basis

## Slide 6
05
Objectives of the GCM Study
The project connects rainfall data, hydrologic calculations and practical system design.
• Analyze rainfall and rainfall intensity patterns for Peshawar
• Estimate rooftop rainwater harvesting potential for each plot size
• Design a safe pipe network for roof runoff conveyance
• Size storage, filtration, first-flush and overflow/recharge components
Deliverables: 30-slide presentation + GCM design report.

## Slide 7
Methodology
06
Methodology
A five-stage workflow converts rainfall records into practical system dimensions.
Data
Collection
Rainfall
Analysis
GCM
Calculations
Pipe
Design
Tank + Filter
Design

## Slide 8
07
Data Sources & Design Assumptions
Assumptions are kept conservative for a residential roof-based harvesting system.
Input | Used in model
Peshawar rainfall data | Annual, monthly and intensity analysis
IDF Development Sheet | Design storm and pipe flow
Regi Model Town by-laws | Roof, plot and free-space areas
Runoff coefficient | 0.85 for roof catchment
First-flush depth | 1.0 mm of roof runoff
Filtration and storage elements are sized after first-flush separation

## Slide 9
08
Rainfall Record: 2002–2024
The GCM model uses 23 years of annual rainfall values for trend, variability and yield calculations.
471 mm
Mean annual rainfall
2003
Wettest year
2021
Driest year
31%
Coefficient of variation

## Slide 10
09
Annual Rainfall Trend
The rainfall record shows strong inter-annual variability, with extreme wet years and dry years.
• Average annual rainfall: 471 mm
• Maximum: 904.5 mm in 2003
• Minimum: 296.4 mm in 2021
• Linear trend: -3.7 mm/year
Design implication: storage and overflow should handle variability rather than depend on a constant yearly supply.

## Slide 11
10
Rainfall Variability & Extremes
Anomaly analysis identifies how far each year moves above or below the long-term mean.
904.5 mm
Wettest year
296.4 mm
Driest year
148 mm
Std. deviation

## Slide 12
11
Monthly Rainfall Distribution
Peshawar rainfall is concentrated in spring and monsoon months.
• March–April: strong spring rainfall peak
• July–August: monsoon contribution and high intensity risk
• Dry months require storage carry-over or municipal backup
Highest monthly event in the series: July 2010 with 294.1 mm.

## Slide 13
12
Seasonal Rainfall Contribution
Rainfall harvesting should be designed for two supply peaks: spring and monsoon.
Season | Mean rainfall | Share
Winter | 110 mm | 23%
Spring | 146 mm | 31%
Monsoon | 182 mm | 38%
Autumn | 36 mm | 8%
Monsoon events dominate peak runoff, while spring rainfall adds important annual supply.

## Slide 14
13
IDF Development Overview
Intensity–duration–frequency curves are used for pipe and overflow design.
• Short storm durations create the highest runoff rates
• Return period selection controls system conservatism
• Gutter, downpipe and overflow should be checked for 10-year, 15-minute intensity
141.6 mm/hr
10-year, 15-min intensity

## Slide 15
14
IDF Curves for Peshawar Station
Intensity drops quickly as storm duration increases.
Return period | 15-min | 30-min | 60-min
2 yr | 51.8 | 32.7 | 20.6
5 yr | 105.8 | 66.7 | 42.0
10 yr | 141.6 | 89.2 | 56.2
25 yr | 186.7 | 117.6 | 74.1
50 yr | 220.2 | 138.7 | 87.4
100 yr | 253.5 | 159.7 | 100.6
Units: mm/hr

## Slide 16
15
Design Storm Selection
For residential roof drainage, the 10-year 15-minute storm is selected as the sizing check.
10-year
Selected storm
15 minutes
Duration
141.6 mm/hr
Intensity
0.85
Runoff coefficient
Q = C × i × A
Q = peak roof runoff, C = runoff coefficient, i = rainfall intensity, A = rooftop area
• Pipe design is based on peak flow, not annual rainfall volume
• Storage sizing is based on monthly/seasonal water balance

## Slide 17
Catchment sizing
16
Rooftop Catchment From Regi By-laws
Rooftop area is converted from square feet to square meters for hydrologic calculations.
Plot | Roof area (ft²) | Roof area (m²) | Free space
5 Marla | 1,020.94 | 94.85 | 340.31 ft²
10 Marla | 1,769.63 | 164.40 | 952.87 ft²
1 Kanal | 3,375.90 | 313.63 | 2,069.10 ft²
Larger roofs generate higher annual yields and higher peak runoff; therefore they need larger tanks and stronger overflow control.

## Slide 18
17
Estimated Annual Harvestable Rainwater
Harvest volume is calculated using mean annual rainfall, roof area and roof runoff coefficient.
Plot | Annual yield | Approx. liters/year
5 Marla | 38.0 m³ | 38,000 L
10 Marla | 65.9 m³ | 65,900 L
1 Kanal | 125.7 m³ | 125,700 L
These volumes are suitable for gardening, floor washing, car washing and toilet flushing after filtration.

## Slide 19
18
Monthly Harvest Potential
Monthly water availability follows rainfall seasonality; tanks should capture spring/monsoon surplus.
• Highest supply months: February–April and July–August
• Low supply months: October–December and May–June
• Larger plots show more reliable non-potable supply

## Slide 20
19
Demand–Use Match
Harvested rainwater should first serve demands that do not require potable quality.
Use | Priority | Treatment need
Garden watering | High | Screen + storage
Car/floor washing | High | Filter + first flush
Toilet flushing | Medium | Filter + disinfection optional
Recharge well | Overflow | Silt removal required
Recommended operation: use the tank for routine non-potable demand and route excess stormwater to recharge after filtration.

## Slide 21
20
GCM Calculation Framework
The GCM converts rainfall inputs into design outputs through four calculation blocks.
Rainfall
Intensity
IDF return period + duration
Calculation
Analysis
Yield, peak flow, water balance
Pipe
System
Gutters, downpipes, collectors
Tank
Design
First flush, filter, storage, overflow
Core formulas
V = P × A × C Q = C × i × A Vff = 1 mm × A
V = volume, P = rainfall depth, A = roof area, C = runoff coefficient, i = intensity, Vff = first-flush volume

## Slide 22
21
Pipe System Design Basis
Pipe capacity is checked against peak roof runoff during a short-duration design storm.
Design parameter | Value
Return period | 10 years
Storm duration | 15 minutes
Rainfall intensity | 141.6 mm/hr
Roof coefficient | 0.85
Pipe material | uPVC / HDPE
Minimum slope | 1:200 to 1:300

## Slide 23
22
Peak Flow & Pipe Sizing
Peak flow increases with rooftop area; pipe layout should split flow across multiple downpipes.
Plot | Q10 peak | Suggested main collector
5 Marla | 3.17 L/s | 110 mm
10 Marla | 5.49 L/s | 160 mm
1 Kanal | 10.48 L/s | 200 mm or 2×160 mm
Use at least two downpipes per roof face where practical; add clean-outs at bends and before the filter chamber.

## Slide 24
23
Recommended Pipe Layout
The layout separates roof capture, first-flush diversion, filtration and tank inflow.
• Gutters sized with freeboard and leaf guards
• Downpipes at corners to reduce roof ponding
• First-flush diverter before filter chamber
• Overflow line routed to recharge/soak pit
Suggested detailing: removable screens, access covers, non-return valves, and silt traps at low points.

## Slide 25
24
First-Flush & Filtration Design
Initial roof runoff is diverted before water enters the storage tank.
Plot | First-flush volume | Filter chamber
5 Marla | 95 L | 1.0 × 0.6 × 0.8 m
10 Marla | 164 L | 1.2 × 0.8 × 0.9 m
1 Kanal | 314 L | 1.5 × 1.0 × 1.0 m
• Filter layers: gravel, coarse sand, fine sand and charcoal
• Provide drain valve for maintenance
• Clean media after major storms

## Slide 26
25
Storage Tank Sizing
Storage is selected to capture usable stormwater while staying practical for plot-scale installation.
Plot | Recommended tank | Annual yield share
5 Marla | 5 m³ | 13%
10 Marla | 10 m³ | 15%
1 Kanal | 20 m³ | 16%
Sizing logic: choose an affordable tank that can store several weeks of non-potable demand and is easy to clean.

## Slide 27
26
Storage & Filtration Tank Designs
RCC underground tanks are preferred for durability; modular HDPE tanks can be used where excavation is limited.
Plot | Tank volume | Typical internal dimensions
5 Marla | 5 m³ | 2.2 × 1.5 × 1.5 m
10 Marla | 10 m³ | 3.0 × 2.0 × 1.7 m
1 Kanal | 20 m³ | 4.0 × 2.5 × 2.0 m or 2×10 m³
• Watertight RCC/HDPE tank with access cover
• Calmed inlet to reduce sediment disturbance
• Pump chamber or gravity outlet depending on plot levels

## Slide 28
27
Overflow & Groundwater Recharge
Overflow should be treated as a design component, not an afterthought.
• Overflow pipe should be at least equal to inlet size
• Route overflow through silt trap before recharge well
• Use gravel-filled recharge pit where soil infiltration allows
• Provide inspection chamber and mosquito-proof venting
Recharge protects the site from surface ponding and supports long-term groundwater conservation.

## Slide 29
28
Operation & Maintenance Plan
A simple maintenance routine keeps harvested water usable and avoids blockages.
Frequency | Action
Before monsoon | Clean roof, gutters and screens
After first heavy rain | Empty first-flush chamber
Monthly | Inspect filter and pipe clean-outs
Quarterly | Remove tank sediment if visible
Annually | Disinfect tank and service pump
O&M note: filtration media should be replaceable without breaking the tank structure.

## Slide 30
29
Key Findings & Recommendations
The GCM confirms that plot-scale rainwater harvesting is technically feasible for Regi Model Town.
38–126 m³
Annual harvest range
3.2–10.5 L/s
Design flow range
5–20 m³
Tank range
95–314 L
First flush range
• Adopt 10-year, 15-minute storm for roof drainage checks
• Install leaf screens, first-flush diverter and graded filter before storage
• Use overflow/recharge pit to reduce drainage load
• Prepare plot-wise drawings before construction and verify soil infiltration
Next step: site survey and final construction drawings for each plot size.

## Slide 31
THANK YOU
Questions & Discussion